## Slide 1
PHASE 1 | NETWORKING | PART 3
IP Addressing
Subnetting & CIDR
IPv4 Structure · Public vs Private · RFC 1918 · Subnet Mask · CIDR · ipcalc · Nmap
IPv4
RFC 1918
/24 CIDR
Subnetting
ipcalc
nmap -sn
AppSec Context
Recon → identify target IPs · CIDR scan for live hosts · Network segmentation = defense · Internal enum after pivot
Aqib
Cybersecurity Student | Pakistan
by Aqib
IP Addressing + Subnetting & CIDR

## Slide 2
by Aqib
IP Addressing + Subnetting & CIDR
SLIDE 02
What is an IP Address?
DEFINITION
Internet Protocol Address — a unique logical identifier assigned to every device on a network.
Think of it as a postal address for your device. Without it, packets have nowhere to go.
IPv4 STRUCTURE — 32 bits / 4 Octets
192
11000000
Network
.
168
10101000
Network
.
1
00000001
Network
.
10
00001010
Host
Each octet: 8 bits → value range: 0 – 255
Total = 2³² = ~4.3 Billion addresses
IPv4
32-bit · 4.3B addresses · Still dominant
Format: 192.168.1.10
IPv6
128-bit · 340 undecillion addresses · Growing
Format: 2001:0db8::1

## Slide 3
by Aqib
IP Addressing + Subnetting & CIDR
SLIDE 03
Public vs Private IP
PRIVATE IP RANGES (RFC 1918)
Not routable on the internet. Internal use only.
/8
10.0.0.0 — 10.255.255.255
Large enterprises / ISP · 16.7M hosts
/12
172.16.0.0 — 172.31.255.255
Medium networks · 1M hosts
/16
192.168.0.0 — 192.168.255.255
Home / Small office · 65K hosts
PUBLIC IP
Assigned by your ISP. Visible on the internet. Unique globally.
This is your attack surface.
cmd: curl ifconfig.me
SPECIAL ADDRESSES
127.0.0.1
Loopback
Your own machine. If this fails — network stack broken.
0.0.0.0
Default Route
'Any destination.' Used in routing tables.
255.255.255.255
Broadcast
Send to all hosts on segment simultaneously.
RECON CONTEXT
Public IP found → attack surface mapped. Private range found (post-pivot) → internal enumeration begins. nmap -sn 10.0.0.0/8

## Slide 4
by Aqib
IP Addressing + Subnetting & CIDR
SLIDE 04
IP Practical — Kali Terminal
Run these on your Kali machine. Understand what every line means.
$ ip addr show
WHAT IT DOES
Shows all network interfaces and their assigned IPs.
LOOK FOR
eth0 = main interface. lo = loopback (127.0.0.1). inet line = your IPv4 address + CIDR.
$ ping 127.0.0.1
WHAT IT DOES
Loopback test — are you pinging yourself?
LOOK FOR
Reply = network stack is alive. Request timeout = something is broken at OS level.
$ ping <metasploitable-ip>
WHAT IT DOES
Test ICMP connectivity to target VM.
LOOK FOR
Reply = machine is reachable. No reply = firewall blocking ICMP or host is down.
$ ip addr show eth0
WHAT IT DOES
Show only eth0 interface detail.
LOOK FOR
Look at inet line → your IP in CIDR format e.g. 192.168.1.100/24 ← that /24 is subnetting.

## Slide 5
by Aqib
IP Addressing + Subnetting & CIDR
SLIDE 05
What is Subnetting?
DEFINITION
Dividing a large IP network into smaller sub-networks. Each subnet is an isolated broadcast domain.
Reason 1 — IP conservation: Don't waste 246 addresses if you only need 10.
Reason 2 — SECURITY:
Contain a breach. If attacker compromises Subnet A — Subnets B and C stay isolated. This is Network Segmentation.
SUBNET MASK — How it works
IP Address
192
.
168
.
1
.
10
Subnet Mask
255
.
255
.
255
.
0
Binary
11111111
11111111
11111111
00000000
← NETWORK PORTION (locked)
HOST PORTION →
RULE:
255 in subnet mask = network bits (fixed). 0 = host bits (variable). First 3 octets = network. Last octet = devices on that network.

## Slide 6
by Aqib
IP Addressing + Subnetting & CIDR
SLIDE 06
CIDR Notation
CIDR — Classless Inter-Domain Routing (IETF, 1993)
Replaced the rigid Class A/B/C system. Notation: IP/prefix-length where prefix = number of network bits.
FORMULA
Total addresses = 2^(32 - prefix)
Usable hosts = 2^(32 - prefix) − 2
(subtract network addr + broadcast addr)
EXAMPLE — 192.168.1.0/24
Prefix /24 → 24 bits = network
8 bits left for hosts → 2⁸ = 256 total
256 − 2 = 254 usable hosts
CIDR REFERENCE TABLE
CIDR
Subnet Mask
Total IPs
Usable Hosts
Use Case
/8
255.0.0.0
16.7M
16,777,214
Large ISPs, enterprise
/16
255.255.0.0
65K
65,534
Campus / data center networks
/24
255.255.255.0
256
254
Typical LAN / home network
/28
255.255.255.240
16
14
Small segments / VLAN
/30
255.255.255.252
4
2
Point-to-point router links
/32
255.255.255.255
1
0 (host)
Single host route

## Slide 7
by Aqib
IP Addressing + Subnetting & CIDR
SLIDE 07
Subnetting Practical — Lab
ipcalc + nmap on Kali against Metasploitable 2
$ ipcalc 192.168.1.0/24
Subnet calculator — breaks down any CIDR block completely.
Network: 192.168.1.0
HostMin: 192.168.1.1
HostMax: 192.168.1.254
Broadcast: 192.168.1.255
Hosts/Net: 254
$ ipcalc 192.168.1.0/28
/28 — much smaller block. Compare output with /24.
Network: 192.168.1.0
HostMin: 192.168.1.1
HostMax: 192.168.1.14
Broadcast: 192.168.1.15
Hosts/Net: 14
$ ipcalc 10.0.0.0/8
Large enterprise/ISP range — see the scale difference.
Network: 10.0.0.0
HostMin: 10.0.0.1
HostMax: 10.255.255.254
Broadcast: 10.255.255.255
Hosts/Net: 16,777,214
$ nmap -sn 192.168.1.0/24
Ping scan — discover all live hosts in subnet. No port scan.
-sn = no port scan (ping only)
Finds Metasploitable 2 IP
ICMP / ARP used for discovery
First step of every pentest
Report: hosts up / down

## Slide 8
SLIDE 08
Key Takeaways
"If you cannot read the network, you cannot attack it. If you cannot attack it, you cannot defend it."
01
IPv4 = 32 bits / 4 octets
Value: 0–255 per octet. Total: ~4.3B addresses. Format: 192.168.1.10
02
Private ranges (RFC 1918)
10.x, 172.16–31.x, 192.168.x — not routable on internet. Your lab network.
03
Subnetting = network division
Subnet mask separates network bits from host bits. Security benefit: segmentation.
04
CIDR /24 = 254 usable hosts
Formula: 2^(32-prefix) − 2. /30 = 2 hosts. /32 = single host.
05
ipcalc + nmap -sn
ipcalc breaks down any CIDR. nmap -sn finds all live hosts — recon step 1.
#IPAddressing
#Subnetting
#CIDR
#NetworkSecurity
#Cybersecurity
#LearningInPublic
Aqib
Cybersecurity Student | Pakistan
by Aqib
IP Addressing + Subnetting & CIDR